## Slide 1
WADF105 | NETWORK SECURITY FUNDAMENTALS
Opening a Secure Website:
Tracing HTTPS Communication Using the TCP/IP Model
Junior Network Analyst Technical Presentation
Student: Muhammad Haseeb
Submission date: 02 October 2026
Notes: Hello, my name is Muhammad Haseeb. I am presenting as a junior network analyst, and I completed this project individually. My scenario is opening a secure website, and I will trace it from the browser to the web server and back, layer by layer, using the TCP/IP model. I will cover DNS, TCP, TLS, encapsulation, addressing, devices, a TCP and UDP comparison, and one real troubleshooting case.

## Slide 2
Communication Scenario: Opening https://example.com
OVERVIEW
1 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
1 URL entered
2 DNS lookup
3 TCP connection
4 TLS handshake
5 HTTPS request
6 Server response
The browser needs the destination IP address, not just the name.
DNS resolution converts the domain name into an IP address.
A transport connection is established to the server, usually on TCP port 443.
TLS authenticates the server and protects the data in transit.
The HTTPS request travels to the web server, and the response returns to the browser.
Notes: The user types a secure URL. A browser cannot send anything to a name, so first it needs the server's IP address, and DNS provides that. Next the browser opens a TCP connection to the server, normally on port 443. Then TLS runs on top of that connection to authenticate the server and set up encryption. Only after that does the browser send the HTTPS request. The web server processes it and sends the response back along the same kind of path. Everything I show later is a closer look at one of these six steps.

## Slide 3
TCP/IP Model and OSI Mapping
MODELS
2 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
TCP/IP layer | OSI layers | Examples in this scenario
Application | 7 Application, 6 Presentation, 5 Session | HTTPS (HTTP + TLS), DNS
Transport | 4 Transport | TCP (port 443), UDP (port 53)
Internet | 3 Network | IP, ICMP
Network Access | 2 Data Link, 1 Physical | Ethernet, Wi-Fi, ARP
Why the difference? TCP/IP was built around working protocols, so functions OSI separates (encoding, session handling) are handled inside application protocols. OSI is a detailed reference model; TCP/IP is the practical model of the Internet.
Notes: TCP/IP is usually shown with four layers and OSI with seven. The Application layer of TCP/IP covers what OSI splits into Application, Presentation and Session, because real protocols like HTTP and DNS handle those functions inside the application. Transport matches OSI Transport. Internet matches OSI Network, where IP lives. Network Access covers Data Link and Physical, for example Ethernet and Wi-Fi. TCP/IP groups layers this way because it was designed around working protocols, while OSI is a more detailed reference model. For my scenario, the examples on the right show where each protocol sits.

## Slide 4
DNS Resolution
APPLICATION LAYER
3 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
Browser
DNS resolver
IP address returned
Browser
query: example.com?
response: IP address
DNS maps a domain name to an IP address; routing needs the IP.
A DNS resolver answers the client query, asking other DNS servers if needed.
DNS is an Application layer protocol.
It commonly uses UDP port 53; TCP port 53 is also used in some cases (for example large responses).
Notes: Humans use domain names, but IP routes packets using addresses, so DNS translates between them. The browser asks a DNS resolver, often provided by the router or ISP. The resolver returns the IP address, possibly after asking other DNS servers. DNS messages commonly use UDP port 53 because queries are small. TCP port 53 can also be used, for example when a response is too large or for zone transfers. DNS is an Application layer protocol. Remember this, because a DNS failure looks like an internet failure to the user but is very different to diagnose.

## Slide 5
TCP Connection Establishment
TRANSPORT LAYER
4 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
Client
Web server :443
1 SYN
2 SYN / ACK
3 ACK
SYN: client requests a connection.
SYN/ACK: server accepts and acknowledges.
ACK: client confirms.
Connection established; data can flow.
HTTPS over TCP uses destination port 443.
Notes: Before any data moves, TCP sets up a connection with a three-way handshake. The client sends a SYN to say it wants to connect and proposes a starting sequence number. The server replies with SYN and ACK, acknowledging the client and sending its own sequence number. The client sends a final ACK. Now both sides have agreed on sequence numbers and the connection is established. For HTTPS over TCP, the destination port is 443 and the client uses a temporary source port. The reliability TCP provides, such as acknowledgements and retransmission, depends on this state.

## Slide 6
TLS and HTTPS
SECURITY
5 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
HTTP data
TLS
Encrypted data
HTTPS communication
HTTP defines web requests and responses (readable if not protected).
TLS provides server authentication, encryption and integrity.
HTTPS = HTTP carried over TLS.
TCP does not encrypt; TLS provides the security.
HTTP/1.1 and HTTP/2 commonly use TCP; HTTP/3 uses QUIC over UDP.
Notes: HTTP defines the request and response messages. On its own it is readable by anyone on the path. TLS sits between HTTP and TCP logically and provides authentication of the server through its certificate, encryption for confidentiality, and integrity checking so tampering is detected. HTTP carried inside TLS is HTTPS. One important accuracy point: TCP does not encrypt anything, TLS does. Also, HTTP/1.1 and HTTP/2 normally run over TCP, whereas HTTP/3 uses QUIC, which runs over UDP and integrates TLS 1.3.

## Slide 7
Encapsulation (Sender) and Decapsulation (Receiver)
ENCAPSULATION
6 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
Application data
DATA
Segment (Transport)
TCP HDR
DATA
Packet (Internet)
IP HDR
TCP HDR
DATA
Frame (Network Access)
FRAME HDR
IP HDR
TCP HDR
DATA
TRAILER
Sender: each layer adds a header as data goes down, then bits are sent. Receiver: decapsulation removes headers in reverse order, up to the application.
Notes: As data moves down the sender's stack, each layer wraps it with its own control information. The application data gets a TCP header with ports and sequence numbers, making a segment. IP adds source and destination IP addresses, making a packet. The network access layer adds an Ethernet or Wi-Fi header with MAC addresses, and a trailer, making a frame, which is sent as bits. The receiver does the reverse, which is decapsulation: it removes the frame header, then the IP header, then the TCP header, and delivers the data to the application. Each layer only reads its own header.

## Slide 8
Original Packet Journey Diagram
PACKET JOURNEY
7 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
HTTPS request (client to server, TCP port 443)
HTTPS response (server to client)
Laptop / Browser
(sender)
Home router
(NAT)
ISP router
Internet routers
Web server
(destination)
Application: HTTPS, DNS
Transport: TCP 443
Internet: IP
Network Access: Ethernet / Wi-Fi
Application: HTTPS, DNS
Transport: TCP 443
Internet: IP
Network Access: Ethernet / Wi-Fi
Layers 1-3 (plus NAT):
forwards by IP,
new frame per link
Internet + Network
Access layers:
forwards by IP
Internet + Network
Access layers:
forwards by IP
IP addresses
Source and destination IP stay the same end to end (NAT rewrites the private source at the home router).
MAC addresses
Used only on each local link, so they change at every hop.
Ports
Client uses a temporary source port; destination is TCP 443.
Notes: This is my packet journey diagram. On the left is the sender, my laptop with the browser and the four TCP/IP layers. The request goes through the home router, the ISP router and Internet routers to the web server on the right, shown by the teal arrow. The orange arrow shows the response returning. Routers work up to the Internet layer: they read the IP header and forward the packet. The source and destination IP addresses stay the same end to end, apart from NAT at the home router, which rewrites the private source address. MAC addresses only identify the next device on each local link, so they change at every hop. The destination port is 443 throughout.

## Slide 9
Protocol Analysis Table
PROTOCOLS
8 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
TCP/IP layer | Protocol | PDU | Addressing information | Purpose
Application | DNS | DNS message | Domain name | Resolves a domain name to an IP address
Application | HTTPS (HTTP over TLS) | HTTP message / TLS record | URL / domain name | Secure web request and response
Transport | TCP | Segment | Port numbers (443) | Reliable, ordered delivery
Transport | UDP | Datagram | Port numbers (53) | Low-overhead delivery (DNS queries)
Internet | IP | Packet | Source / destination IP | Routing between networks
Network Access | Ethernet / Wi-Fi | Frame | Source / destination MAC | Delivery on the local link
Network Access | ARP (IPv4) | ARP message | IP to MAC | Finds next-hop MAC address
Notes: This table summarises the protocols in my scenario by layer. For each one I list the protocol data unit, the addressing information it uses and its purpose. DNS and HTTPS are Application layer. TLS protects the HTTP data. TCP uses port numbers and its unit is the segment. IP uses source and destination addresses, and its unit is the packet. Ethernet or Wi-Fi uses MAC addresses and its unit is the frame. ARP is a small helper that finds the MAC address of the next hop on an IPv4 local network. Note that QUIC and HTTP/3 are the modern alternative over UDP.

## Slide 10
TCP vs UDP
TRANSPORT LAYER
9 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
Feature | TCP | UDP
Connection | Connection-oriented (handshake) | Connectionless
Reliability | Acknowledgements, retransmission | No delivery guarantee
Ordering | Sequence numbers, ordered delivery | Not ordered
Overhead | Higher (20+ byte header, state) | Lower (8 byte header)
Examples | HTTPS (443), SSH (22) | DNS (53), online gaming, real-time media
UDP is not simply "faster": it has lower overhead and no TCP reliability mechanisms, so applications choose it for timeliness or build their own recovery. HTTP/3 uses QUIC over UDP.
Notes: TCP is connection-oriented: it uses a handshake, sequence numbers, acknowledgements, retransmission and ordered delivery, with flow and congestion control. UDP is connectionless and gives no delivery, ordering or retransmission guarantees. UDP is not simply always faster. It has lower protocol overhead and no setup delay, so applications that prefer timeliness, or that handle loss themselves, use it. HTTPS and SSH use TCP. DNS queries and real-time media or gaming commonly use UDP. HTTP/3 shows the idea in modern form: QUIC, over UDP, builds its own reliability and encryption.

## Slide 11
Realistic Communication Failure: DNS Resolution Failure
FAILURE SCENARIO
10 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
User
Browser
DNS resolution
DNS FAILURE
Website unavailable
Symptom: https://example.com does not open, though other connectivity may work.
Cause: the client cannot resolve the name, so no TCP connection is attempted.
Realistic causes: unreachable DNS server, wrong client DNS setting, wrong DHCP or router DNS configuration.
Key point: a DNS failure is not the same as a general internet connectivity failure.
Notes: The failure I chose is a DNS resolution failure. The user types https://example.com, but the client cannot turn the name into an IP address, so the browser never even starts a TCP connection. This is realistic because DNS servers can be unreachable, DHCP can hand out wrong DNS settings, or the client can be misconfigured. The important point is that the network may still be fine. A user may say the internet is down, but traffic to IP addresses could work perfectly. The job of the analyst is to tell these two situations apart.

## Slide 12
Troubleshooting the DNS Failure
TROUBLESHOOTING
11 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
1 Identify
ipconfig /all
Check IP, gateway and DNS servers.
Note symptom: site will not open.
2 Diagnose
ping 8.8.8.8 (IP path)
nslookup example.com (DNS)
IP works but DNS fails: check DNS server, client settings, router/DHCP.
3 Resolve
Correct the DNS configuration, or use a functioning resolver suited to the network.
4 Verify
nslookup example.com
Reopen https://example.com
These are diagnostic tests: their results decide the diagnosis. A successful ping to 8.8.8.8 does not prove DNS works; nslookup testing the name does.
Notes: I follow four stages: identify, diagnose, resolve, verify. First, identify the symptom: the site does not open. Check the client configuration with ipconfig slash all, to see the IP address, gateway and DNS servers. Then test IP connectivity with ping 8.8.8.8. If that works, routing works. Then test name resolution with nslookup example.com. If IP works but nslookup fails, the problem is DNS. Note ping to an IP address does not prove DNS works, and these are diagnostic tests, not proof until I see the results. Then I check the DNS server settings and availability on the client, router and DHCP. To resolve, I correct the DNS setting or use a working resolver suited to the network. To verify, I run nslookup again and reopen the website.

## Slide 13
Complete Communication Process and Conclusion
SUMMARY
12 / 12
Muhammad Haseeb | Opening a Secure Website: HTTPS and the TCP/IP Model
URL entered
DNS resolves
TCP connect
TLS secure
HTTPS request
Encapsulate
Routers forward
Server decapsulates
Response returns
Browser displays
Application: defines the HTTPS and DNS messages.
Transport: delivers between processes using ports (TCP 443).
Internet: IP addressing and routing between networks.
Network Access: moves frames across each local link.
Notes: To summarise the whole journey: the user enters a URL, DNS resolves the domain, TCP builds a connection, TLS secures it, and the browser sends the HTTPS request. Each layer encapsulates the data, and routers forward the packets using IP addresses, with new frames on each link. The web server decapsulates the data, processes the request and sends the response, which returns the same way and is decapsulated by the browser. The layers cooperate: Application defines the message, Transport delivers it between processes using ports, Internet routes it between networks, and Network Access moves it across each link. Thank you, and I am happy to answer questions.

## Slide 14
References
RFC 9293: Transmission Control Protocol (TCP). IETF, 2022. https://www.rfc-editor.org/info/rfc9293
RFC 768: User Datagram Protocol. IETF, 1980. https://www.rfc-editor.org/info/rfc768
RFC 791: Internet Protocol. IETF, 1981. https://www.rfc-editor.org/info/rfc791
RFC 1035: Domain Names, Implementation and Specification. IETF, 1987. https://www.rfc-editor.org/info/rfc1035
RFC 8446: The Transport Layer Security (TLS) Protocol Version 1.3. IETF, 2018. https://www.rfc-editor.org/info/rfc8446
RFC 9114: HTTP/3. IETF, 2022. https://www.rfc-editor.org/info/rfc9114
AI-use declaration: An AI assistant was used to help organise the presentation, explain networking concepts and draft wording. I reviewed and verified the technical content against the references above and remain responsible for this submission.
Notes: These are the official IETF standards behind each protocol I described. I also declare that AI assistance was used to organise and draft the material, and that I reviewed and verified the content myself. Thank you.